| 64 31 081 | Removing and installing/replacing microfilter housing (upper section) |
| --- | --- |

|  | Release screws (1). Unfasten screws (2 and 3). Remove upper section of microfilter housing (4). Installation: Make sure upper section of microfilter housing (4) is correctly seated. |
| --- | --- |
|  | Replacement: Release catches (1). Release microfilter (2) in direction of arrow from upper section of housing (3). Installation: Make sure microfilter (2) is correctly seated. |

| 64 31 010 | Replacing microfilter for interior ventilation |
| --- | --- |

|  | Important! Risk of damage! A/C system must not be operated without the prescribed filter element. Follow manufacturer's instructions. |
| --- | --- |
|  | Necessary preliminary tasks: • Remove microfilter housing (upper section) |

|  | Release catches (1). Release microfilter (2) in direction of arrow from upper section of housing (3). Installation: Make sure microfilter (2) is correctly seated. |
| --- | --- |

| 64 31 092 | Removing and installing/replacing microfilter housing (lower section) |
| --- | --- |

|  | Necessary preliminary tasks: • Remove upper section of microfilter housing |
| --- | --- |
|  | Release holder (1). Release catches (3). Remove right cover (2). Installation: Make sure right cover (2) is correctly seated. |

|  | Left cover (4) is removed in same way as right cover. Also for E90: Release cable holder (2) and remove hose (1) from cover (4). Installation: Make sure cable holder (2) and hose (1) are correctly seated in opening (3). |
| --- | --- |
|  | E8x: Unfasten plug connection (1) and disconnect. Unclip cable from guides (2). |

|  | E8x: Open hose clamps (2) on hose (1). |
| --- | --- |
|  | Press detent lugs (3). Release cable strip (1) in direction of arrow from lower section of microfilter housing (2). Installation: Retaining lugs (3) must not be damaged or missing. Make sure cable strip is correctly seated. |

|  | Release holder (2) on both sides. Release screw (1) on both sides on lower section of microfilter housing (3). |
| --- | --- |
|  | Feed out microfilter housing lower section (1) in direction of arrow and remove. Installation: Make sure microfilter housing lower section (1) is correctly seated. |

|  | Installation: Seal (2) of microfilter housing lower section (1) must not be damaged or missing. |
| --- | --- |